## Slide 1
Germany PCM Case Build
From raw public data to consistent nodal and zonal HOPE cases
Core design rule
Build one nodal master case first, then derive the zonal case mechanically.
Nodal Buses
783
Nodal Lines
1174
Generators
4135
Demo Cost
$10.00M
Network backbone: OSM Europe transmission dataset + PyPSA-Eur reference workflow
Fleet: powerplantmatching with Germany-specific validation layers
Chronology: SMARD national load + generation and four TSO load helper files

## Slide 2
Executive Summary
How the Germany case was assembled and why the design is comparison-friendly
Goal
Create one canonical Germany PCM dataset that supports both nodal and zonal analysis.
Method
Freeze every major mapping once: generator -> bus -> zone -> zonal derivative.
Outcome
A solved 2-day nodal demo case plus a consistent 4-zone zonal comparison case.

## Slide 3
Source Stack
Each layer was chosen to keep the zonal case derived from, not detached from, the nodal case
Network
OSM Europe transmission dataset
PyPSA-Eur workflow reference
Fleet
Power plant matching
BNetzA validation support
Chronology
SMARD Germany load + generation
SMARD TSO load helper files
Map Geometry
Germany state boundary GeoJSON
reconstructed 4-TSO overlay

## Slide 4
Integration Architecture
The zonal case is produced by aggregation from the nodal master case
Raw Sources
Cleaned Staging
Frozen Maps
Nodal Master
Zonal Derivative
Network cleaner produces stable buses, lines, transformers, and links.
Fleet cleaner assigns each generator to one nodal bus and inherits one zone tag.
Chronology builder freezes one 2025 hourly basis and optional zonal load shares.
Zonal seams and capacities are derived from the nodal cross-zone structure.

## Slide 5
Build Steps
Six steps turned raw public data into the Germany PCM comparison set
1
Network backbone
Normalize OSM Europe inputs and keep a connected 783-bus Germany network.
2
Bus-zone mapping
Freeze one Bus_id -> TSO zone table for 50Hertz, Amprion, TenneT, and TransnetBW.
3
Generator mapping
Clean powerplantmatching and assign each plant to a nodal bus once.
4
Chronology
Build one 2025 hourly chronology with 8760 rows and reuse it everywhere.
5
Case assembly
Build the canonical nodal case first and aggregate the zonal case from it.
6
Dashboard geometry
Reconstruct a file-backed Germany TSO overlay from state boundaries and frozen bus geography.

## Slide 6
Case Snapshot
Current master and derivative cases in the repo
Nodal Master Case
Zonal Derivative Case
783 buses
1174 lines
4135 generator entries
8760-hour canonical chronology
4 zones
5 interzonal interfaces
46 zonal generator entries
Derived from nodal geography and seams
Design choice: the zonal case is not independently calibrated; it is aggregated from the nodal master dataset.

## Slide 7
Assumptions And Caveats
Important choices to explain when comparing Germany nodal and zonal results
Frozen Modeling Choices
Current Caveats
Use one nodal master case as the canonical truth source.
Use four TSO research zones instead of the real DE-LU bidding zone.
Keep representative-day modes off for PCM debug validation windows.
Preserve chronology consistency before adding more model complexity.
The Germany TSO dashboard overlay is reconstructed, not official GIS.
The 2-day nodal demo case is solve-proven; longer nodal horizons still need staged validation.
Generator validation against MaStR and Kraftwerksliste can still be deepened.
Historical benchmarking should keep expanding as the case matures.

## Slide 8
Debugging Journey
The nodal case became usable after fixing topology and electrical scaling
Initial failure
Disconnected components, singular-network behavior, and severe angle-limit pathologies.
Core fixes
Transformer connectivity, largest connected component, and HOPE-scale reactance normalization.
Usable result
A 1-day and then 2-day full-nodal Germany debug run solved cleanly with zero load shedding.

## Slide 9
Solved Demo Outcome
2-day January nodal case used for the current Germany dashboard demo
Solve Window
48 hours
Total Cost
$10.00M
Load Shedding
0.0
Dashboard Status
Default case
Chart: Operating cost by zone
| 50Hertz | Amprion | TenneT | TransnetBW
Operating cost ($M) | 2.5975 | 1.839 | 3.784 | 1.7764
Why this matters
The solved 2-day nodal case is stable enough to demo the Germany dashboard while the longer nodal horizon is still being staged.

## Slide 10
Next Steps
What to improve next in the Germany case build
Data QA
Deepen plant validation and benchmark chronology totals against SMARD.
Nodal Scale-Up
Extend from short-window nodal success toward longer production horizons.
Geometry
Swap the reconstructed TSO overlay for official GIS if a public layer appears.
Storytelling
Compare nodal and zonal outputs directly in the dashboard and in papers.

## Slide 11
Key Files In The Repo
Useful paths for updating the Germany build and the dashboard story
Build workspace
E:/MIT Dropbox/Shen Wang/MIT/RA/HOPE_project/tools/germany_pcm_case_related
Dashboard geometry
E:/MIT Dropbox/Shen Wang/MIT/RA/HOPE_project/tools/hope_dashboard/data/germany_tso_zones.geojson
Nodal master case
E:/MIT Dropbox/Shen Wang/MIT/RA/HOPE_project/ModelCases/GERMANY_PCM_nodal_case
Zonal derivative case
E:/MIT Dropbox/Shen Wang/MIT/RA/HOPE_project/ModelCases/GERMANY_PCM_zonal4_case

## Slide 12
Raw Input Snapshot
What went into the Germany build before cleaning and integration
Raw buses
12,936
Raw lines
16,050
Raw transformers
1,949
Raw fleet rows
165,064
Cleaned staging outputs
791 cleaned network buses and 1,019 cleaned lines
155 cleaned transformers and 791 bus-zone assignments
141,420 cleaned generator rows and 8,760 canonical hourly records
SMARD generation file: 8,766 raw rows before trimming to the canonical 8,760-hour basis.
Each SMARD TSO load helper file: 8,766 raw rows before chronology normalization.
The raw-to-clean reduction is intentional: the HOPE case keeps only Germany-relevant, schema-consistent, and solve-ready records.

## Slide 13
Processing To The Current Case
How the raw files become the current Germany nodal and zonal HOPE cases
1
Ingest raw sources
OSM network tables, powerplantmatching fleet, SMARD chronology, and reference geometry.
2
Normalize schemas
Rename columns, coerce coordinates, standardize technology and status fields, and filter to Germany.
3
Repair the network
Keep transformer connectivity, remove disconnected leftovers, and rescale branch reactance for HOPE.
4
Freeze spatial maps
Create one Bus_id -> Zone_id table and one generator -> bus mapping table.
5
Build chronology
Normalize Germany hourly load and generation, then create zonal helper load shares.
6
Assemble cases
Build the nodal master case first, then derive the 4-zone case and the dashboard geometry from it.

## Slide 14
Open-Source Case Comparison
Where this Germany HOPE case sits relative to other open-source electricity-model case frameworks
Case / framework | Primary focus | Geographic style | Why it matters here
This HOPE Germany case | Consistent nodal-vs-zonal PCM comparison | Germany nodal master plus derived 4-zone case | Built specifically to compare dispatch, congestion, and price outcomes under matched assumptions
PyPSA-Eur | Reproducible Europe-wide workflow and scenario engine | Europe-wide network with flexible clustering | Best backbone reference for open data retrieval and preprocessing structure
eTraGo / open_eGo | High-resolution Germany-centered planning and sector coupling | Germany detailed, foreign system aggregated | Strong Germany data model and nodal optimization context
POMATO DE example | Market design, FBMC, redispatch, and zonal analysis | Germany / European market-study orientation | Strong reference for zonal market-coupling and redispatch analysis

## Slide 15
Comparison: Pros And Trade-Offs
Why we still built a custom HOPE Germany case instead of using one of the open models directly
HOPE Germany case
Pros
Direct nodal-vs-zonal comparability
Same chronology and asset assumptions in both cases
Trade-offs
Short nodal solve horizon is solved and demo-ready, but longer horizons still need staging
PyPSA-Eur
Pros
Excellent open workflow, clustering, and data-pipeline reference
Trade-offs
Not a drop-in HOPE PCM case and not tailored to Germany 4-TSO nodal-vs-zonal comparison
eTraGo / open_eGo
Pros
Rich Germany-specific data model and strong nodal / planning context
Trade-offs
Heavier stack, database dependence, and broader scope than the focused HOPE comparison case
POMATO DE example
Pros
Strong market-coupling, FBMC, and redispatch framing
Trade-offs
Different modeling stack and case objective than our HOPE PCM comparison build